## Slide 1: Using Carbon-Based Advanced Treatment (CBAT) to Implement "One Water" Initiatives
Chamindra Dassanayake (CD), PhD, PE
Wendell Khunjar, PhD, PE

## Slide 2: Presentation Outline
UOSA
SWIFT
Gwinnett County
Aurora
Water Factory 21
Treatment Drivers
Lessons from CBAT
The Future
Carbon Based Advanced Treatment 101
Full-scale CBAT installations
Pilot-scale CBAT investigations

## Slide 3: Treatment Drivers

## Slide 4: Unique Drivers Influence Movement toward Advanced Water Treatment
Drought
Cost of Production/Supply
Subsidence
Industrial/Alternative Demand
Environmental Discharge

## Slide 5: Carbon Based Advanced Treatment
In 101 Seconds

## Slide 6: Historically, Two Main Paradigms for AWT
Membrane-based
Carbon-based
Chemical Barrier
Pathogen Barrier
Notes: Removal of microbial and chemical constituents
Multi-barrier approach
Monitorable performance

## Slide 7: Deciding Between Treatment Paradigms
Influent water quality
State Mandate for Treatment
Aquifer Compatibility
Distribution System Compatibility
TDS Reduction Needs
Concentrate/
Residual Management?
Resilience
mBAT
cBAT

## Slide 8: Deciding Between Treatment Paradigms: State Requirements, Site Specific Needs
Example: Pathogen Inactivation Log Reduction Values
 | California |  |  | Texas | Florida | Colorado
Reuse Type: | IPR (GW) | IPR (SW) | DPR | IPR or DPR | Draft DPR | DPR
Starting Point: | Raw WW |  |  | Treated WW | Raw WW | Treated WW
Enteric Viruses | 12-log | 8 to 9-log | 20-log | 8-log (min.) | 8 to 12-log | 8 to 12-log
Giardia | 10-log | 7 to 8-log | 14-log | 6-log (min.) | 6 to 10-log | 6 to 10-log
Cryptosporidium | 10-log | 8 to 9-log | 15-log | 5.5-log (min.) | 5.5 to 10-log | 5.5 to 10-log
Additional state-specific requirements for number & type of chemical control barriers
CBAT
> 12
> 10
> 10
Notes: Highlight the TX column
Pull this down to the Franklin and GCDWR examples
Did not do microbial sampling at Franklin
Used CT approach
Show the CBAT removal potential relative to the TX
xBAT can also be footprint intensive with clarification

## Slide 9: Deciding Between Treatment Paradigms State Requirements, Site Specific Needs – HYBRID AWT
The California DPR approach to realize benefits from carbon-based in concert with membrane-based treatment trains
Ozone
Biologically
Active
Filtration
Ultrafiltration
Reverse Osmosis
Ultraviolet Disinfection Advanced Oxidation
Secondary or Tertiary Effluent
Pure Water San Diego
Potential Benefits
Improved RO permeate quality
Improved RO concentrate quality
Lower membrane costs
 | CA
Reuse Type: | DPR
Starting Point: | Raw WW
Enteric Viruses | 20-log
Giardia | 14-log
Cryptosporidium | 15-log
Notes: Brine – main driver

## Slide 10: Deciding Between Treatment Paradigms: Flexibility!
For inland utilities, need treatment concepts that support multiple end use opportunities :
  Non-potable Reuse
  Groundwater Augmentation
  Surface Water Augmentation
  Raw Water Augmentation
Also minimize concentrate/residual disposal challenges
Carbon Based Advanced Treatment can be advantageous

## Slide 11: Evaluating Outcomes from Multiple Perspectives
What is the influent water quality, what are the effluent water quality targets, what are the risks, and what tools (processes) do I have to produce the desired water?
How do I balance water and wastewater needs, what option is the most cost-effective, and what option best supports the mission of the utility and our end users?
What option protects public health and the environment and how will the facility be permitted and monitored?
Where is my water coming from and do I trust my utility to reliably provide clean drinking water and effectively manage wastewater at an affordable price?
Consultant
Utility
Regulator
Public
What are the risks; what are the barriers; how are the barriers monitored; and what happens if a barrier fails?
Hazard Assessment and Critical Control Points (HACCP)

## Slide 12: CBAT Has An Established Track Record
Project | Year | Application | Capacity (mgd) | Scale | Status
National |  |  |  |  | 
Upper Occoquan Service Authority (UOSA), VA | 1978 | IPR | 53 | Full | Operational
Fred Hervey WRF, El Paso, TX | 1985 | IPR | 10 | Full | Operational
F. Wayne Hill WRC, Gwinnett County, GA | 2006 2016 | IPR DPR | 60 - | Full Pilot | Operational Study Completed
Hamby WRF, Abilene, TX | 2015 | IPR | 7 | Full | Operational
Rio Rancho, NM | 2017 | IPR | 1 | Full | Operational
PureAlta, Altamonte Springs, FL | 2017 | DPR | - | Pilot | Operational
Hampton Roads Sanitation District (HRSD) SWIFT, VA | 2018 2026 | IPR/DPR IPR | 1 16 | Demo Full | Operational Under Construction
Colorado Springs, CO | 2021 | DPR | - | Pilot | Completed
South Jordan, UT | 2022 | DPR | - | Pilot | Operational
Anne Arundel, MD | 2023 | IPR | - | Pilot | Operational
Clay County, FL | 2023 | DPR | - | Pilot | Under Construction
Polk County, FL | 2023 | DPR | - | Pilot | Operational
Franklin, TN | 2023 | PR | - | Pilot | Study Completed
Pure Water San Diego, CA | 2011 2025 | IPR IPR | 1 34 | Demo Full | Operational Design
International |  |  |  |  | 
Goreangab WRF, Windhoek, Namibia | 2002 | DPR | 5.5 | Full | Operational
Eastern Treatment Plant, Melbourne, Australia | 2013 | NPR | 92 | Full | Operational
Neugut WWTP, Dubendorf, Switzerland | 2018 | NPR | 15 | Full | Operational
Cape Town, South Africa | 2026 | DPR |  | Full | Design
CBAT configuration is adaptable
CBAT is a robust treatment platform that can be further enhanced
CBAT is not proprietary

## Slide 13: Lessons from CBAT

## Slide 14: CBAT in Practice!
Direct potable reuse since 1960s using CBAT
Upgraded in 2000
Windhoek, Namibia – Goreangab Water Reclamation Plant
Upper Occoquan Service Authority
Surface water augmentation in practice since 1978
WW discharge limits set to improve reservoir health and downstream drinking water treatment

## Slide 15: Case Studies
Gwinnett County, GA – F. Wayne Hill WRC

## Slide 16: FWHWRC – CBAT for IPR
Added Ozone/BAC to meet stringent COD limits; now seeing IPR benefits with surface water augmentation of Lake Lanier
Process treatment train at the F. Wayne Hill Water Resources Center
Notes: Piloted DPR – Gaya to send slides

## Slide 17: FWHWRC – CBAT and DPR
Courtesy GCDWR, Gaya Ram Mohan, Kati Bell
15% FWHWRC Blend
50% FWHWRC Blendx
100% FWHWRC
Met ALL primary and secondary MCLs evaluated
Nitrate, Bromate, Color, Manganese, NDMA > MCL or action levels
Nitrate, Bromate, Cyanide > MCL levels
https://www.waterrf.org/research/projects/demonstration-high-quality-drinking-water-production-using-multi-stage-ozone
All blends: biological parameters were below detection
All blends: DBPs were low

## Slide 18: Case Studies
Franklin, TN

## Slide 19: City of Franklin, TN - CBAT Considered to Meet Multiple Objectives and Potential End-Points
  Irrigation: Expand the use of reclaimed water for landscape and other irrigation
  Recreation: Use purified water to increase flows in the Harpeth River
  Augmentation: Use purified water to increase availability of source water to the Water Treatment Plant

## Slide 20: TN Did/Does Not Have Potable Reuse Guidelines
Reference: USEPA REUSExplorer

## Slide 21: Long-Term CBAT Pilot Conducted to Support Permitting
Multi-barrier Treatment Approach

## Slide 22: CBAT Pilot Pictures
Ozone Contactor
BAF
GAC
Tertiary Membranes

## Slide 23
Pilot Summary
Ozone
Ozone:TOC ratio contact time, CT, LRV
BAC
HLR, EBCT, Supplemental C dose, Feed DO, backwash criteria
GAC
EBCT, upstream water quality, bed volumes
UVAOP
UV dose, peroxide dose, upstream water quality
Bench Scale
Nutrient Removal
Ozone-BAC
Organics and Nutrients
GAC
CECs
UVAOP
CECs
N and P
TOC/DOC, TN
Organics Removal
Microbial Inactivation
Lessons learned translate to design criteria for individual processes to meet treatment objectives.
AWT Process capable of producing high quality effluent:
TOC ≤ 3 mg/L
UVT > 94%
TSS < 1 mg/L
TN ≤ 2 mg/L
TP ≤ 2 mg/L
CECs - Met Target Log Reduction / MCLs
  > 97% reduction of PPCPs
Notes: Algal bioassays – improved discharge water body quality
Highlight which of these aligned with TCDEQ requirements

## Slide 24: Pilot Summary
PFOA and PFOS removed to below 4 ng ng/L

## Slide 25: Pilot Summary
HAA and TTHM < MCLs
Nitrosamines removed to between 1 and 2 ug/L

## Slide 26: Pilot Summary
HAA and TTHM < MCLs
Nitrosamines removed to between 1 and 2 ug/L

## Slide 27: Summary and Future Considerations
Notes: DPR paradigm

## Slide 28: The Future of AWT is Bright!
CBAT has an established track record
CBAT configuration is adaptable
CBAT is a robust treatment platform that can be further enhanced
CBAT is not proprietary
  Diversity in mechanisms (oxidation, separation, adsorption) to accomplish log reductions of chemical and microbial contaminants
  Always room for improvement and refinement!
  Minimize bromate formation / ozone control and minimization of other regulated and unregulated DBPs
  Increase reduction of 1,4-dioxane
  Optimize pathogen LRVs
  Organics pre-treatment
  TDS
Notes: CBAT is good base-case
Hybrid options can get us intensified benefits
Salt management options
40% cheaper  mBAT (FWH)
Potable reuse stds for TX – TCDEQ for Bustamante
Can meet requirements – need to pilot
Can address the salt piece – doesn’t generate ROC; however, weakness is no TDS reduction
Footprint also positive

## Slide 29: Using Carbon-Based Advanced Treatment (CBAT) to Implement "One Water" Initiatives
Chamindra Dassanayake (CD), PhD, PE
cdassanayake@hazenandsawyer.com
Wendell Khunjar, PhD, PE
wkhunjar@hazenandsawyer.com
Gaya Ram Mohan
grammohan@hazenandsawyer.com